## Slide 1: CASALS
Jiageng Zhong
2026

## Slide 2
CASALS architecture
CASALS (Concurrent Artificially-intelligent Spectrometry and Adaptive LiDAR System) is designed to acquire co-registered structure (range/waveform) and reflectance information over the same ground swath.
Primary CASALS LiDAR
Laser transmitter: wavelength-tuned pulsed emission (swath encoding)
Dispersive scan optics: λ→θ beam steering (cross-track swath, no scanner)
Receiver + detector: multi-channel, grating-filtered return capture
Electronics/FPGA + digitizer: time-tagging + full-waveform acquisition (range-gated)
Airborne demo / measurement suite
GNSS/INS (Applanix): pose/time for geotagging and georeferencing
Co-aligned hyperspectral imager (Headwall): VNIR–SWIR reflectance over the LiDAR swath
Look-ahead cameras (concept/flight suite): context imaging for real-time targeting decisions

## Slide 3
Observation principle
How CASALS forms a swath
Single beam, many footprints: CASALS sweeps laser wavelength, and a grating maps wavelength to cross-track angle, creating a dense footprint set across the swath.
Track concept: a sweep visits many cross-track footprint locations; successive sweeps can “fill” the swath (SCBI waveforms note).
Full-waveform LiDAR: each footprint returns a digitized analog waveform (vs. photon list), supporting canopy/ground separation and complex scenes.

## Slide 4
CASALS specifications
Spaceflight concept / targets (scalable track count)
Wavelength-to-angle swath mapping: fast wavelength tuning + dispersive grating in the telescope (no mechanical scanner).
Cross-track capacity (concept): a 30-nm tuning range can form ~1,200 resolvable cross-track spots over 0.825° (~7.2 km swath from 500-km orbit); any subset can be selected by wavelength switching.
Key implication: “track count” is a design degree of freedom (up to ~1,200 resolvable spots in the cited concept), not inherently fixed at 256.
Airborne prototype / datasets (256-track implementation)
Operating wavelength (prototype for Earth science): 1040 nm.
Channelization: 256 tuned wavelengths across ~13 nm; 2-ns pulse carved at each wavelength; amplified up to 3 kW peak power (design).
Receiver filtering/detection: grating-spectrometer receiver with ~0.8-nm passband per footprint; HgCdTe APD array; signals time-division multiplexed to two high-speed ADCs; range-gated digitization to reduce data volume.
Airborne geometry @ 8.5 km: 0.67° total scan angle using 256 tuned wavelengths; ~110 m swath width; ~0.7 m overlapping footprints; ~0.43 m cross-track and ~0.24 m along-track spacing; waveform per footprint with ~20 detected photons (reported).
Airborne geometry @ ~5 km (SCBI note): 0.75° full-width scan; 32 footprints per sweep and 8 sweeps fill the swath to 256 overlapping footprints; ~0.24 m cross-track spacing; ~0.17 m along-track spacing at 80 m/s; ~65 m swath (and “equivalent” ~6.5 km from 500 km orbit).

## Slide 5
Airborne / UAV observation mode
Cross-track steering: 256 tuned wavelengths spanning 0.67° total scan angle, yielding ~110 m swath from 8.5 km altitude.
Footprint geometry (demo): ~0.7 m diameter overlapping footprints; ~0.43 m cross-track and ~0.24 m along-track spacing.
Co-boresighted passive sensors: Headwall VNIR–SWIR pushbroom + frame cameras; frame cameras point ~7° ahead to give ~8 s for onboard analysis/retargeting.

## Slide 6
Airborne / UAV observation mode
Wavelength-tuning points the laser beam cross-track over a full-width angle of 0.75° (0.013rad).
One tuning sweep targets 32 footprint locations distributed with equal spacing across the swath and 8 sweeps fill in the swath cross-track with 256 overlapping footprints.
The cross-track footprint spacing is 0.24m at 5km ranging distance, equal to the FWHM diameter, forming a 65m wide swath (equivalent to 6.5km swath in 500km satellite orbit).
The along-track footprint spacing is 0.17m at 80m/s aircraft ground speed, forming 256 parallel tracks.
12 of 256 Wavelength-tuned Tracks
Across the Airborne CASALS Lidar Swath

## Slide 7
Nadir-port window reflections
A “nadir-port window” is a protective optical window in the nadir viewing path. A small fraction of the laser pulse can reflect off that window surface(s) and re-enter the receiver path, creating a strong instrumental ghost (non-geophysical) at a consistent range/time.
Possible ways to detect:
fixed range bin / early-time consistency
abnormal amplitude
weak dependence on scene
track-localized behavior
Range (m) →
Track Index

## Slide 8
Georeference
Time-tagged LiDAR data (Tx start time + Rx samples) + platform navigation (position/attitude). Airborne demo explicitly uses Applanix POS AVX 510 and reports ~1 m footprint geolocation accuracy (1σ) from 8.5 km, with over-water maneuvers to estimate pointing biases.
Steps:
Time alignment: synchronize LiDAR row/footprint timestamps to GNSS/INS time.
Range retrieval: estimate range to scattering surfaces from waveform timing relative to start pulse (Tx) and Rx gate.
Pointing model: convert wavelength channel → cross-track angle (calibrated wavelength-to-angle map) + apply attitude (roll/pitch/yaw) + boresight.
Ray–surface intersection: intersect LOS with Earth ellipsoid/DEM (or use waveform-derived range to solve 3D point along the LOS).
Calibration/refinement: solve residual biases (boresight, lever-arm, timing) using dedicated maneuvers / control surfaces; propagate uncertainties to products.

## Slide 9
Airborne / UAV observation mode

## Slide 10
Airborne / UAV observation mode

## Slide 11
Airborne / UAV observation mode

## Slide 12
Airborne / UAV observation mode

## Slide 13
Airborne / UAV observation mode

## Slide 14
Airborne / UAV observation mode

## Slide 15
Airborne / UAV observation mode

## Slide 16
Airborne / UAV observation mode